## Slide 1: Concurrent engineering approach to design mission feasibility studies at CNES
JL. Le Gal
Plateau d’Architecture des Systèmes Orbitaux
Centre National d’Etudes Spatiales

## Slide 2: The Toulouse Space Centre
Leads
Develops
Ensures
the orbital system Projects
(satellites and onboard payloads, ground segments)
satellite station acquisition
& keeping operations
technical policy
preparation of the future
and executes scientific
balloon-borne experiments
use of data and
innovative applications

## Slide 3: Content
PASO and the Concurrent Engineering Facility
Concurrent Engineering Process
  The engineering satellite model
  Description of the mission
Partners and lessons learned

## Slide 4: PASO (Plateau d’Architecture des Systèmes Orbitaux)
Goal : To assess feasibility of space mission candidates
  To support programme directory for programme decision with technical and cost expertise,
  To support science team in their proposal to Calls,
  To identify technology activity or possible usage of new concepts.
Organization :
  An office with full time engineers,
  a cost estimation unit,
  a group of 60 expert engineers (in technical departments),
  A Concurrent Design Facility (CIC : Centre d’Ingénierie Concourante).
Yearly :
  ~10 – 15 studies
  ~20 – 30 fte
  ~1 M€ for contract support

## Slide 5: PASO studies
A plan of studies of new missions or new concepts in order to
  Build phase A programme decision
  Help to define CNES position on programmatic or technical aspects
Navigation
Telecommunications
Security
Defense
Earth observation climate
Sciences
Universe


## Slide 6: General approach for mission assessment
Mission
Definition
Review
Mission Advisory Group (user representatives, customers…)
CNES team, partners, industry support …
Phase 2,3
Analysis, comparison of scenarios,
Optimisation and selection
Phase 1
Identification of drivers (mission, program, technical) and scenarios

## Slide 7: CIC (Centre d’Ingénierie Concourante )

## Slide 8: CIC : Multi-touch screen
Hardware : PQ Labs TM kit
Software : SHELL-MT TM
Multi-touch on traditional applications
Example :
- touchDown with one finger -> left mouse-click pressed
- TouchUp with one finger -> left mouse-click released
- TouchPinch between 2-10 fingers -> left mouse-click released at the pinch + mouse roll
Mapping file
multi-touch interactions
keyboard/mouse actions

## Slide 9: Preparation of CIC sessions
Needs
Mission Group
Client
PASO Group
Programmatics
Param. 1 (Resolution)
Param. 2
(Spectral Bands)
Param. 3
…
Param. 1 (Orbit)
Param. 2
(Platform)
Param. 3
…
Param. 1 (Cooperation)
Param. 2
(Launch Date)
Conf B
Perfo ?
Cost ?
Budgets ?
Technics
Conf C
Perfo ?
Cost ?
Budgets ?
Conf A
Perfo ?
Cost ?
Budgets ?
OPTIONS

## Slide 10: Content
PASO and the Concurrent Engineering Facility
Concurrent Engineering process
  The engineering satellite model
  Description of the mission
Partners and lessons learned

## Slide 11: CIC Approach
2 models implemented :
  - Description of the satellite
  - Description of ephemeris of mission phases
The base consists of a set of files based on implementation of standards :
ECSS-ETM-10-25A :
Engineering design model data exchange
CIC exchange protocol
Collaborative creation of a technical reference allowing establishment of satellite budgets :

## Slide 12: Content
PASO and the Concurrent Engineering Facility
Concurrent Engineering process
  The engineering satellite model
  Description of the mission
Partners and lessons learned

## Slide 13: Description of the satellite based on the ECSS-ETM-10-25A standard
System Engineering
Information Model
(SEIM)
Space Engineering
Reference Data Library
(SERDL)
XML model,
Web Services…

## Slide 14: IDM-CIC : A structured and shared View of the satellite
Excel description of : - equipments, - sub-systems, - payload, - satellite, - mission phases to perform budgets : - Mass Center and Inertia - consumed power - propellant
- … - …

## Slide 15: IDM-CIC approach
Data
Exchange
Payload
AOCS
System
Data-handling
Thermal
Configuration

## Slide 16: IDM-CIC : Geometric representation

## Slide 17: IDM-CIC / SketchUp coupling

## Slide 18: IDM-CIC : Synchronisation of IDM model with the CAD model
CATIA file
IDM-CIC workbook
STEP file
Export / Import
functions

## Slide 19: IDM-CIC View

## Slide 20: Content
PASO and the Concurrent Engineering Facility
Concurrent Engineering process
  The engineering satellite model
  Description of the mission
Partners and lessons learned

## Slide 21: CIC exchange prototol to describe ephemeris
A solution based on CCSDS* standard
* Consultative Committe for Space Data Systems
CIC protocol
Position and velocity data :
OEM file
Attitude data :
AEM file
Complementary data :
(geometrical, thermal, electrical..)
MEM file

## Slide 22: CIC files
HEADER
METADATA
DATA

## Slide 23: CIC exchange protocol (extract)
Geometrical data
AOCS data
Thermal data
Electrical data
Communication data

## Slide 24: VTS-CIC : Visualization of mission phases
Mistigri_OEM.txt
Mistigri_AEM.txt
SatelliteConsumedPower_MEM.txt
AngleSunNormSA1_MEM.txt
Time /CMD
Time /CMD
Time /CMD
Time /CMD
Download VTS :
http://logiciels.cnes.fr/VTS/fr/index.html

## Slide 25: Content
PASO and the Concurrent Engineering Facility
Concurrent Engineering Process
  The engineering satellite model
  Description of the mission
Partners and lessons learned

## Slide 26: Partners
Coordination of ECSS development
Students users
IDM-CIC development
VTS-CIC development
Advanced multi-touch solution
Industrial partners and users
STEP development interface
Development of interface with analysis tools

## Slide 27: Lessons learned
The approach is based on the establishment of :
a shared data set,
and implementation of consultation tools, easy to use, which are important to communicate.
To be effective, the working sessions must be prepared :
the working hypotheses,
and data which experts have to produce,
should be clearly defined.
The collaboration is based on the implementation of standard data and each technical expert must know exchange to contrebute to the establishment of the reference base.

## Slide 28: Conclusion
CIC approach is an approach of management of project :
The technical compromises are understood and accepted by all,
Contributions of experts are valued because directly visible at the system level,
The planning of the working sessions imposes the pace of the study.
This approach implemented internally is also an effective way that enables collaboration with our partners.

## Slide 29: Thank You for your attention