## Slide 1: Part 21 Edition 3
“Crowd sourcing massive product models”
Dr. Martin Hardwick
President STEP Tools, Inc.
Team Leader ISO STEP-Manufacturing
Professor of Computer Science, RPI

## Slide 2: Crowd Sourcing Massive Product Models
Design of a complete aircraft, ship or vehicle
Manufacturing operations across a supply chain
Construction of a skyscraper
The models are massive
The models are made by thousands and used by millions

## Slide 3: Available Elements
Extensible information models
  STEP for design
  STEP-NC for manufacturing
  IFC for building and construction
  Other file types – JT, XML, 3DPDF etc
CAD, CAM and BIM systems that can make data for very large fragments of the models

## Slide 4: Design goals of Part 21 Edition 3
Massive Product models
  Support data linking outside of a CAD system
  Enable the use of URI’s and URL’s
  Divide large files into multiple smaller files
Crowdsourcing
  Add intelligence using JavaScript
  Light weight, open-source binding
  Quick and easy data manipulation
Upward and downward compatible with e2 and e1

## Slide 5: Anchors and References
ISO-10303-21;
HEADER;
FILE_DESCRIPTION( ... )
FILE_NAME( ... );
FILE_SCHEMA ( ... );
ENDSEC;
ANCHOR;
<tool_tip_face> = #100;
<tool_tip_usage> = #100;
<tool_tip_unused> = $;
ENDSEC;
REFERENCE;
#1234 = <http://www.tool.com/mill#bottom_face>;
#1235 = <http://www.tool.com/mill#bottom_face_rep>;
ENDSEC;
DATA;
#100= CHAIN_BASED_GEOMETRIC_ITEM_SPECIFIC_USAGE
( . . ., #1234, (#1235,#22,#23) . . .);
ENDSEC;
END-ISO-10303-21;

## Slide 6: Model Population
Model population is
  All data sections in current file
  All data sections in referenced files
  All data sections in files listed in a schema_population
Workpiece STEP File
Workplan
STEP-NC File
Link File
“Orphaned” without
the schema_population
Massive product model

## Slide 7: ZIP Archives
ISO-10303-21;
HEADER;
ECMASCRIPT (‘constraints.js’);
ENDSEC;
ANCHOR;
<as1_pe >= #as1_pe
REFERENCE;
#as1_pe = <assembly.stp#root>;
#bolt = <part/bolt.stp#bolt>;
#nut = <part/nut.stp#nut>;
#rod = <part/rod.stp#rod>;
#plate = <part/plate.stp#plate>;
#l-bracket = <part/l-bracket.stp#l-bracket>;
ENDSEC;
END-ISO-10303-21;
Archive
(as1.stpz)
Directory
(ISO-10303-21.txt)

## Slide 8: Multi-File References
Anchor can be referenced from other file types
Reference can be to another file type
Reference format resolved by protocols and mime types
ANCHOR;
<tool_tip> = #100; /* Can be referenced from JT or XML */
ENDSEC; /* E.g. <mill#tool_tip> */
REFERENCE;
#1234 = <http://www.tool.com/holder.jt#bottom_face>;
ENDSEC;

## Slide 9: JavaScript
Function to connect a workpiece to a workplan
function linker(model, workplan, workpiece, type)
{
with workpiece.anchor.$type.credentials {
if (stage != 'manufacturing')
return null;
if (status != 'released')
return null;
}
with model.reference {
if (name != 'as_is shape' && name != 'to-be shape' && name != 'removal shape') // alternate is to check using a mapping table compiler
return NULL;
if (workpiece.anchor.$tag.shape.type != 'product_definition_shape') // alternate is to check using an EXPRESS compiler
return NULL:
if (workpiece.anchor.$tag.shape.geometry != 'advanced_boundary_representation') // application constraint
return NULL;
name = type;
shape = workpiece.anchor.shape;
exec = workplan.anchor.executable; // checking this left as an exercise for the reader
workplan.schema_population.set_population ((new P21.Population).set_uri (model)); // add this link to the population of the workplan
return model;
}
}

## Slide 10: JavaScript demonstrations http://www.steptools.com/demos/

## Slide 11: CAM Tooling Pilot
Job
Shop
CAM
STEP-NC File
Tool
Vendor
CAM
STEP-NC File
Make operations with generic tooling
SaveAs STEP-NC
Make tooling recommendations
SaveAs STEP-NC with optimal process
15% better machining*
*average
STEP Tool 1
STEP Tool 2
E3 linking

## Slide 12: Summary
Edition 3 adds intelligent interfaces to STEP, STEP-NC and IFC
  Massive shared product models
  Open and closed loop manufacturing
Next steps are
  Review of current draft by TC184/SC4 in Paris
    http://www.steptools.com/library/standard
  Verification with open source examples
  Submit for ballot as DIS

## Slide 13: Backup

## Slide 14: Part 21 Editions 1 & 2
Very successful - edition 1 in 1994, edition 2 in 2002
  Implemented by all the CAD, CAM and BIM vendors.
  Upward compatible across many, many enhancements.
  Very fast implementation by translation systems.
Designed for easy implementation
  Minimal data format for maximal upward compatibility.
  No URI’s, OIDs of other fancy features.
  No concessions to easy data presentation.

## Slide 15: Known Issues
The information models are supported by a file format that was designed to be written by one system in its entirety, and read by another system in its entirety.
The information models are hard to program because of all the requirements that must be met to avoid ambiguity and enable extensibility.